## Slide 1
Smart Temperature Monitoring System
-USING BOLT IOT
-By B.J.DINESH KUMAR

## Slide 2: MONITORING A COOLING CHAMBER USING IOT
To maintain the chamber between -40 to -30 degrees Celsius.
Alert if the temperature reaches above or below the threshold.
To maintain a log of when the cooling chamber for the production of the tablets is opened.
In the below examples we use Home refrigerator instead of cooling chamber and their values.

## Slide 3: Objectives and their execution

## Slide 4: 1. Building the circuit for temperature monitoring system, using the Bolt and LM35 sensor.
Circuit connection of LM35 using Bolt IOT
LM35
Bolt module
Female to male wire

## Slide 5
It consist of a LM35 (temperature sensor) to get the temperature.
A female to male connector is used to interface the sensor to the bolt wi-fi module:
-> Using male to female wire connect the 3 pins of the LM35 to the Bolt Wi-fi Module as follows:
    VCC pin of the LM35 connects to 5v of the Bolt Wi-fi module
    Output pin of the LM35 connects to A0 (Analog input pin) of the Bolt Wi-fi module.
    Gnd pin of the LM35 connects to the Gnd.

## Slide 6: 2.Creating a product on the Bolt Cloud, to monitor the data from the LM35, and link it to your Bolt.

## Slide 8: 3.Writing the product code, required to run the polynomial regression algorithm on the data sent by the Bolt

## Slide 9: 4.the temperature monitoring circuit is kept inside the fridge with the door of the fridge closed, and let the system record the temperature readings for about 2 hours.
Monitoring circuit inside the refrigerator

## Slide 10
Temperature is recorded for two hours inside the fridge

## Slide 11: 5.A python code is written which will fetch the temperature data every 10 seconds and send out an email alert, if the temperature goes beyond the temperature thresholds which we determined from Using the reading that was received in the 2 hours.

## Slide 13: 6.The python code is modified,to also do a Z-score analysis and print the line “Someone has opened the fridge door” when an anomaly is detected. The Z-score analysis code is tuned such that it detects an anomaly when someone opens the door of the fridge

## Slide 17: The following are the screenshots of the sensor working with the modified code.
The code is executed in unbuntu and the data is collected

## Slide 18
Mail is sent when someone opens the fridge door and as well as when the temperature exceeds the threshold limit

## Slide 19
Point of anomaly
Prediction and anomaly detection in visual representation

## Slide 20
This is the response mail which is sent to the user if someone opens the fridge door or when the temperature crosses the threshold.

## Slide 21: Conclusion:
This can be implemented in large scale using the same method.
Eliminates the use of manpower to monitor the temperature constantly.
Immediate notification in-case of an alert.

## Slide 22
THANK YOU